## Slide 1: Bosch XDK

## Slide 2: Introduction
The XDK 110 Cross-Domain Development Kit is a prototyping platform for Internet of Things (IoT) use cases. It works with Windows 7 or higher.
It thereby allows users a step in-between the first hardware prototype and series production, or simply as the first compact prototype.
The device was built in a way that Bosch can easily adapt the product for mass production and the users unique sensor requirements.
The XDK110 creates the opportunity for users to try out more advanced programming on the device itself to realize a sensor which processes data and reportsevents instead of simply transmitting raw data.

## Slide 3: Built-in sensors
Accelerometer
Acoustic sensor
Digital light sensor
Gyroscope
Humidity
Magnetometer
Pressure
Temperature

## Slide 4: User interface
Power switch
Green system LED to display the state of charging
3 programmable status LEDs (red, orange, yellow)
2 programmable push-buttons
Micro SD card slot
Interface for J-Link Debug-probe
Interface for extension board

## Slide 5: Software
Free software download for XDK110 & XDK Node from the website (https://xdk.io/software-downloads).
Integrated development environment supplied with XDK Workbench (Eclipse)
LWM2M communication protocol
Extensive libraries and modular source code enable the developer to fully understand the system
Datagram Transport Layer Security (DTLS)

## Slide 6: LED State
LED green:
LED green:
LED yellow:
LED yellow:
LED red:
State | Meaning
Continuous | Charging/Charging suspended by thermal loop
Flashing | Safety timers expired
Off | Charging done/Recharging after termination/IC disabled or no valid input power/Battery absent
State | Meaning
Continuous | Bootloader mode active and USB connected; Driver loaded
State | Meaning
Continuous | Bootloader mode active
Flashing 5x | No valid application detected; XDK remains in bootloader mode

## Slide 7: Getting started
Start the software "XDK Workbench"
The "Welcome" screen will appear
If an XDK is connected, the XDK symbol will appear
Create your application
Click on the "Flash" Button. Your application will be transferred to the XDK
Check the output of the XDK by using the console of the "XDK-Workbench"

## Slide 8: Flashing the XDK 110
The XDK 110 can only be programmed while in bootloader mode. To enter bootloader mode, press the "Flash" button. The software puts the XDK 110 in bootloader mode, flashes the program and reboots. If the software does not put the XDK 110 in bootloader mode, this can be done manually:
Switch off the XDK 110
Press Button 1
Hold down Button 1 and switch the XDK 110 back on
The red LED will light up. If a USB connection is already established, the yellow LED will also light up. Press the Flash button.

## Slide 9: Benefits
All-in-one sensor kit: no need for component selection, hardware assembly, or deployment of a real-time operating system
Algorithm library
Example code in open source licensing
Drivers for all system components included
Secure data protocol
Built-in lithium ion rechargeable battery
Functional extendibility via the included extension board
High-level API for the standard user and low-level API for the power user
PC and MAC based development tools for Windows, LINUX and MacOS make it an easy to work with tool for any developer