## Slide 1: ERBESSD INSTRUMENTS Phantom

## Slide 2: Introduction
Phantom Expert is a Triaxial Wireless Vibration Sensor able to send 3 simultaneous FFT and Time waveform recordings at once.
This wireless Vibration Sensor wake up on high vibration levels in order to send data and alarms.
This sensor have a built-in integrator, as a result, it can internally calculate velocity parameters for alarms.

## Slide 3: User Interface
Analyse and visualize the data of the sensors with DigivibeMX.

## Slide 4: Main Features
Full waveform and spectrum data
Programmable Internal RMS Trigger
Selectable measurement range up to 32G
Configurable Alarm interval
Standby mode and long battery life
Selectable Recording time 1s / 2s / 4s / 8s / 16s
Configurable Measurement Interval
Speed + Vibration Integration
Configure your sensor using your mobile
IP67 Design for protection from liquid and dust

## Slide 5: Gateway Initial Configuration
First the gateway will have to be connected to a computer via a USB. Then, restart you Gateway trough the pinhole on the left side of the screen using a paperclip.
Select the Gateway device as a Wi-Fi network connection. The password of the Gateway network is “88888888”.
Once connected to the Phantom Network, go to Start and click on Control Panel. Proceed to click “View network status and tasks” in Control Panel window.
Once “Network and Sharing Center” window is opened, click on “Change adapter settings”. This will open the “Network connections” window. Here double click Ethernet.
In the Ethernet Properties window, select “Internet Protocol version 4 (TCP/IPv4)”. In the next window. Select “Use following IP address” and type the desired IP address in the box.
The Subnet Mask will be generated automatically and then type the desired Default Gateway. Click “Ok”.

## Slide 6: IP Configuration
Once our network settings are configurated, open a web browser window and access to 192.168.4.1 to open the Gateway configuration page from Erbessd Instruments. Here, select “Static IP configuration”.
Type the IP address you previously typed in the “Internet Protocol version 4 (TCP/IPv4)” but with a variant in the last numbers. Type the same Subnet mask and Default Gateway.
The last step, select “Static Monitor” and in the Monitor IP address type the correct IP address of the “Internet Protocol version 4 (TCP/IPv4)” window and then click “Save Settings”.
Then connect the Gateway with the Ethernet cable to the computer. This will make the device restart again. Once the device is restarted the screen will show the Gateway IP.
Once that the Gateway IP is shown on the screen, open the EI Monitoring software and click the green button to start service.

## Slide 7: Phantom Configuration
On the DigivibeMX go to the configuration window menu, select preferences and go to the phantom tab, once there, check the box with the option “Show phantom menu” and click “ok” to save changes.
Now, the Phantom menu will show in the window’s menu bar. Go to the phantom window and select Wizard.
The Phantom Configuration Wizard screen opens in a new window. Click the Next button.
Following we need to add our phantom device, in the select phantom window we have the next options:
Option A allows us to manually enter a phantom code, and with option B we can scan the phantom QR code.

## Slide 8: Adding Manually
You can add phantoms by using an 11-digit ID code, select the Manually button: The Code window opens.
Manually enter the 11-digit Phantom ID code from the sensor’s QR label (2-digit sensor model code + 9-digit sensor serial number) into the Code text field. Then click the Ok button.
The manually entered sensor will appear in the Phantoms added section. Sensors may be removed from the group using the Delete option.

## Slide 9: Scanning the QR code
(PC, laptop, or tablet computer camera required): Click the QR Code Reader button. The Code Bar Reader window opens.
Select the desired camera from the Device dropdown list. Position the QR label in front of the camera – squarely and close enough to be clearly read.
The Code Bar Reader window will automatically capture the image, momentarily turn green, and document the sensor when it has read the QR code.
It will then close automatically, and the scanned sensor will appear in the Phantoms added section.

## Slide 10: Naming and Configuration
The Set Phantom screen allows users to identify Phantoms using common nomenclature, for easier identification in DigivibeMX Phantom.
The phantom can be organized with the following tools:
With the group box, you can select a previously group name from the list or type a new one to create a group.
In the name box, select a name for the device to simplify the phantom identification.
On the description box, select what kind of phantom that is being used.
the Interval Send data establishes the sensor’s collection interval. The minimum value for data collection is 10 minutes, and the maximum is 1,440 minutes (1 day).

## Slide 11: Set the Axis and Alarms
Select the phantom alarms window. This window has two options, the Axis configuration, and the alarms.
In the Axis configuration, select a value for each phantom axis, you can set horizontal, vertical, or axial from the displayed list.
In alarms, you can set a preset RMS and temperature threshold. If the alarm value is exceeded, the sensor will immediately wake and send an unscheduled data collection.

## Slide 12: Completing Phantom Configuration
The Completing Phantom Configuration screen provides an opportunity to add a new phantom sensor and review the sensor configurations.
If corrections need to be made, the previous button can be used.
If satisfied with the configuration, click Finish to save all changes and close the wizard.