## Slide 1: MultiTech Conduit IP67 Base Station

## Slide 2: Introduction
MultiTech Conduit IP67 Base Station is a ruggedized IoT gateway solution, specifically designed for outdoor LoRa® public or private network deployments.
This highly scalable and certified IP67 solution is capable of resisting the harshest environmental factors including moisture, dust, wind, rain, snow and extreme heat, supporting LoRaWAN® applications in virtually any environment.
The enhanced Conduit IP67 solution can support thousands of LoRaWAN certified end nodes, including the MultiTech mDot and xDot.
This flexible solution provides durable, low-power, wide area connectivity in support of M2M and IoT applications for both LoRa service providers and individual enterprises wanting to expand their LoRa network coverage.
Designed for easy deployment, the solution includes a MultiTech Conduit with a LoRa MultiTech mCard™ , IP67 enclosure, LoRa antenna to improve outdoor range and Ethernet or optional 4G-LTE backhaul.
It can be deployed as part of an existing telecommunications tower, individual stand or wall mount.

## Slide 3: Benefits
Greatly expands LoRa network coverage
External antenna increases LoRa connectivity to remote assets
Improved design enhancing thermal performance and easy external port access to SIM and USB connectors

## Slide 4: Features
14 dBm support for European region
Certified for Europe 868 MHz ISM bands
ISM band scanning for optimum LoRa performance
Listen Before Talk operating protocol
GNSS for location coordinate information

## Slide 5: Requirements
In addition to the Base Station and included accessories, you will need:
PoE Injector. For requirements, refer to Conduit IP67 Base Station PoE Application Note (S000678).
Cat 5 or greater Ethernet cable rated for outdoor use.
Micro SIM (3FF) card for LTE models. MultiTech recommends using a SIM card rated for the climate where the device will be installed.
14awg or larger ground wire with a closed loop terminal. For details, go to Installing a Ground Wire in this document.
Phillips screwdriver.

## Slide 6: Connecting Ethernet
To connect your Ethernet cable and PoE injector:
Remove the sealing nut, clamping claw, and sealing insert.
Thread the Ethernet cable (not provided) through the sealing nut.
Wrap the sealing insert around the cable and the clamping claw over the sealing insert.
Plug the Ethernet cable into the Ethernet port.
Push the seal and clamping claw into the cable gland body.
Push the sealing nut over the insert and clamping claw and tighten on the cable gland body to 10.5 lbf in (12.0 kgf cm).

## Slide 7: Installing a Micro SIM Card
To install a SIM card:
Remove the SIM/USB cover. The SIM holder is above the USB port.
Gently push the micro SIM card into the holder with the cut corner to the left and the SIM contacts facing towards the USB port as shown.
Reattach the plastic cover and tighten to 10.5 lbf.in (12 kgf.cm).

## Slide 8: Installing a Ground Wire
Proper grounding of the metal enclosure is required to ensure safety. There are two ground lugs and one ground screw located on the enclosure back.
Connecting a ground lug to an earth ground is the recommended method.
Ground wire (not provided) must be suitable for outdoor location and meet a minimum wire gauge of 14awg or larger.
Use the supplied ground screw to fasten wire. Ground wire terminal (not provided) must be closed loop and corrosive free in design.
Insert screw through loop terminal and fasten to 17.28 kfg.cm. You can use either ground lug with the ground screw to connect the ground wire to the enclosure.

## Slide 9: Attaching the Mounting Bracket
To attach the mounting bracket to the Base Station: Attach the bracket to the back of the Base Station using the supplied screws and washers as shown.
To attach the Base Station on a pole: Attach the Base Station to the pole using the supplied hose clamps as shown.
To mount the device on a wall: Use the four bracket tabs to attach the Base Station to the wall with the supplied screws and anchors as shown below.

## Slide 10: Attaching Antennas
After mounting the Base Station:
For LTE models, attach the LTE cellular antennas to the Cell and Diversity connectors on the bottom of the Base Station.
Attach the GPS antenna to the GPS connector on the top of the Base Station.
For Wi-Fi/Bluetooth models, attach the Wi-Fi antenna to the Wi-Fi connector on the top of the Base Station.
Attach the LoRa antenna(s) to the LoRa and connectors at the top of the Base Station. If only one LoRa antenna, install on LoRa connector.
If attaching LoRa antennas away from the Base Station, go to Attaching LoRa Antennas via Cable.
Go to Connecting Ethernet for steps on connecting the Base Station to power and Ethernet.

## Slide 11: Attaching LoRa Antennas via Cable
After attaching other antennas:
Use an antenna hose clamp to attach the antenna bracket to a LoRa antenna.
Attach the lightning arrestor (optional) to the antenna.
Attach coaxial antenna cable to the lightning arrestor.
For a pole mount, use hose clamps to mount the antenna mounting bracket to the pole. For a wall mount, attach the antenna bracket to the wall using the four tabs on the bracket.
If you have a second LoRa antenna, repeat Steps 1 – 4 for the second LoRa antenna.
Attach the antenna cable to the LoRa connector. If you have a second LoRa antenna, connect to the second LoRa connector.