## Slide 1: Pycom LoPy4

## Slide 2: Introduction
The LoPy4 is a quadruple bearer MicroPython enabled development board (LoRa, Sigfox, WiFi, Bluetooth).
With the latest Espressif chipset the LoPy4 offers a perfect combination of power, friendliness and flexibility.
This allows the user to create and connect your things everywhere.

## Slide 3: Features
Powerful CPU, BLE and state of the art WiFi radio.
Simultaneous LoRa and Sigfox connectivity.
Can also double up as a Nano LoRa gateway

## Slide 4: Programming the device
UART
By default, the modules run an interactive python REPL on UART0 which is connected to P0 (RX) and P1 (TX) running at 115200 baud.
The easiest way to connect to the LoPy4 is via our expansion board, but any USB UART adapter will suffice.
Code can be run via this interactive REPL or you can use our PyMakr plugin for Atom or Visual Studio Code to upload code to the board.
Wi–Fi
In older modules, the FiPy by default acts as a Wi-Fi access point. SSID: fipy-wlan-XXXX Password: www.pycom.io.
Newer modules come pre-loaded with the Pybytes firmware that allows configuring the device OTA through an existing WiFi AP via SmartPhone.
See https://docs.pycom.io/smart for details. Once connected to the FiPy’s Wi-Fi network you can access it in two ways.

## Slide 5: Programming the device
Continued from previous slide
Telnet
Running on port 23 is a telnet server. This acts in a very similar way to the UART. It presents you with an interactive REPL and can also be used to upload code via PyMakr.
FTP
The LoPy4 also runs a FTP server that allows you to copy files to and from the device, include an SD card if one is connected.
To connect to this FTP server, you need to use plain FTP (un–encrypted) with the following credentials: User: micro Password: python

## Slide 6: Boot modes
Bootloader mode
In order to update the firmware of the LoPy4 device, it needs to be placed into bootloader mode.
In order to do this, P2 needs to be connected to ground when the device reboots. Once in bootloader mode you can use the Pycom firmware update tool to update to the latest official firmware.
If you are developing your own firmware based on our open–source firmware, a flashing script is provided with the source code.
Safe boot
The micropython firmware features a safe boot feature that skips the boot.py and main.py scripts and goes straight to the REPL.
This is useful if the device is programmed with code that causes the device to crash or become inaccessible. To access this mode, you need to connect P12 to 3.3V and reset the device.
Upon entering safe boot mode, the on–board LED will begin to blink orange. Depending on the duration the pin is held at 3.3V, a different firmware will be run.

## Slide 7: Power
The LoPy4 features an on–board voltage regulator that takes 3.5V – 5.5V from the VIN pin and regulates it to 3.3V.
It is important to only use the 3.3V as an output and not try to feed 3.3V into this pin as this could damage the regulator.

## Slide 8: WiFi
Supported features
802.11 b/g/n/e/i
802.11 n (2.4 GHz), up to 150 Mbps
802.11 e: QoS for wireless multimedia technology
WMM–PS, UAPSD
A–MPDU and A–MSDU aggregation
Block ACK
Fragmentation and defragmentation
Automatic Beacon monitoring/scanning
802.11 i security features: pre–authentication and TSN
Wi–Fi Protected Access (WPA)/WPA2/WPA2–
Enterprise/Wi–Fi Protected Setup (WPS)
Infrastructure BSS Station mode/SoftAP mode
Wi–Fi Direct (P2P), P2P Discovery, P2P Group Owner mode and P2P Power Management

## Slide 9: Bluetooth
Supported features:
Compliant with Bluetooth v4.2 BR/EDR and BLE specification
Class–1, class–2 and class–3 transmitter without external power amplifier
Enhanced power control
+12 dBm transmitting power
NZIF receiver with –97 dBm sensitivity
Adaptive Frequency Hopping (AFH)
Standard HCI based on SDIO/SPI/UART
High–speed UART HCI, up to 4 Mbps
BT 4.2 controller and host stack
Service Discover Protocol (SDP)
General Access Profile (GAP)
Security Manage Protocol (SMP)
ATT/GATT
HID
All GATT–based profile supported
SPP–like GATT–based profile
BLE Beacon
A2DP/AVRCP/SPP, HSP/HFP, RFCOMM
CVSD and SBC for audio codec
Bluetooth Piconet and Scatternet