## Slide 1: Sentrius RG186

## Slide 2: Introduction
The Sentrius RG186 LoRa-Enabled Gateway from Laird is the ultimate in secure, scalable, robust LoRa solutions for end-to-end control of your private LoRaWAN network.
It also offers enterprise dual-band Wi-Fi, BT v4.0 (BLE and Classic) and wired Ethernet for complete design freedom.
Based on the Semtech SX1301/SX1257 chipset designs, it offers a LoRa range up to 10 miles and pre-loaded LoRa Packet Forwarder software, perfect for highly scalable, flexible IoT networks.

## Slide 3: Main Features
Aggregate and utilize IoT data.
Multiple interface options for ultimate design choice.
Comprehensive security and reliability.
Broad certifications and approvals.
Platform for building actionable IoT intelligence.
Personal support for your implementation.

## Slide 4: Connecting the Hardware
Connect the gateway: To use the gateway, you must power up the gateway and access the web interface via the Ethernet port. To do this, follow these steps:
1. Follow the label on the box and connect the three (or 4 with RG1291+LTE) antennas. Refer to Antenna Configuration section for additional information.
2. Connect the power supply.
3. Connect the gateway to your router (#3 in Figure 3) using the Ethernet cable.

## Slide 5: SIM Card Installation
To utilize the LTE functionality, a cellular network provider’s SIM card needs to be installed into the gateway.
The recommended SIM card to purchase shall support LTE-CAT 1, in order to utilize the full capabilities of the LTE gateway.
To install the SIM card, follow these steps:
Unscrew the four (4) back Torx screws using a T8 Torx screwdriver for the non-IP67 gateway version.
Carefully move the top enclosure lid to the back of the gateway for the indoor (non-IP67) version as seen below.
If replacing the production installed SIM card, punch out the Micro-SIM (3FF size) from the Main Sim card (secondary set of punch out lines from the center moving outward).
Install the SIM card into the SIM card slot in the upper right location near the LTE modem making sure the copper contact side of the SIM card is facing down (follow Blue Arrow). Re-close the gateway and screw down the screws when complete.

## Slide 6: Antenna Configuration
To configure the antenna properly, take the following steps:
Attach the two shorter antennas to the 2.4/5.5 GHz (Wi-Fi) ports.
Attach the third and longer antenna to the 868 MHz/900 MHz (LoRa) port.
Attach the fourth and wider blade antenna to the LTE port.

## Slide 7: Wi-fi Configuration
The gateway includes a mode to allow you to configure without ethernet access, in the case that you wish to join a wireless network.
Apply power to the gateway and allow to start, then perform the following:
Depress and hold the user button for seven seconds.
From a wirelessly enabled device perform a scan.
Connect to the access point rg1xx29378B, where 29378B are the last six digits of the Ethernet MAC address found on the label on the bottom of the gateway.

## Slide 8: Log into the Gateway
To log into the gateway web interface, follow these steps:
Determine the last three bytes of your gateway’s Ethernet MAC address. This can be found on the label on the bottom of the gateway; the last three bytes are highlighted.
Enter the URL into the web browser to access the web interface. For example, for the gateway used in this guide, the URL is https://rg1xx29378B.local., where “29378B” are the last six digits of the Ethernet MAC address. In Wi-Fi quick config mode, the gateway can also be accessed via the IP address at https://192.168.1.1
Accept the self-signed security certificate in the browser
Click Advanced
Click Proceed
Log on using the following default credentials: Username: sentrius Password: RG1xx. After logging in, the program warns you to change the default credentials for security reasons. Only one login session is allowed at a time.
If there is another active session active, the program warns you before allowing you to take over the session
Click Continue to log in.

## Slide 9: Lan Connection Setup
The LAN menu allows selections for configuration and status of the IPv4/IPv6 wired network. The current status of the IPv4 network is also displayed. To access this section, click LAN in the page menu.
The first page for configuring the Ethernet LAN connection is the IPv4 Configuration page. There are two basic modes of operation – DHCP and Static.
These are selected in the IP Address Acquisition Method drop-down box. The gateway factory default setting is DHCP.
DHCP – When in DHCP mode, all settings are provided by the DHCP server. All configuration settings (except IP Address Acquisition Method) are greyed out. IP values provided by DHCP are displayed but cannot be changed.
When the IP Address Acquisition Method is set to static, all IP settings are fixed and saved in the device.
The external Gateway IP address is optional and may be left blank. DNS Server IP addresses are also optional. Zero, one, or two DNS servers may be specified.

## Slide 10: IPv6 Configuration
Select the IPv6 configuration by clicking the IPv6 menu item in the side menu of the LAN view.
DHCP – In DHCP mode, all settings are provided through communication with an IPv6 server on the network.
Auto – In auto mode, you have the option of selecting the auto DHCP method (either stateless or SLAAC). At this time, IPv6 static mode is only partially supported.

## Slide 11: Wi-fi Connection Setup
By default, the gateway’s Wi-Fi radio is not configured to connect to a Wi-Fi network. The user must access the web interface on the gateway via the Ethernet interface to setup the Wi-Fi connection.
To setup a Wi-Fi connection, click the Wi-Fi tab in the main menu. In the sidebar on the left, you can navigate to various Wi-Fi pages and see the status of the Wi-Fi interface.
There is also a button to enable/disable the Wi-Fi radio.
In the sidebar on the left, you can navigate to various Wi-Fi pages and see the status of the Wi-Fi interface.
There is also a button to enable/disable the Wi-Fi radio.